## Slide 1: Intro to RISC-V (California Gold)

## Slide 2: Floating Point Discussion
Floating Point Discussion
The RISC-V Instruction Set Architecture
Elements of Architecture: Registers
Add/Sub Instructions
Immediates

## Slide 3: Floating Point Fallacy
FP add associative?
  x + (y + z) = –1.5x1038 + (1.5x1038 + 1.0) = –1.5x1038 + (1.5x1038) = 0.0
  (x + y) + z = (–1.5x1038 + 1.5x1038) + 1.0 = (0.0) + 1.0 = 1.0
Therefore, Floating Point add is not associative!
  Why? FP result approximates real result!
  With bigger exponents, step size between floats gets bigger, too!
  This example: 1.5 x 1038 is so much larger than 1.0 that 1.5 x 1038 + 1.0 in floating point representation rounds to 1.5 x 1038.
x
– 1.5 x 1038
y
1.5 x 1038
z
1.0

## Slide 4: Rounding
When we perform math on real numbers, we have to worry about rounding to fit the result in the significand field.
The FP hardware carries two extra bits of precision, and then rounds to get the proper value
Rounding also occurs when converting:
  double to a single precision value, or
  floating point number to an integer
Under the hood

## Slide 5: IEEE FP’s Four Rounding Modes
Round towards +∞
  ALWAYS round “up”: 2.001  3, -2.001  -2
Round towards –∞
  ALWAYS round “down”: 1.999  1, -1.999  -2
Truncate
  Just drop the last bits (round towards 0)
(default) Unbiased. If midway, round to even
  Normal rounding, almost: 2.4  2, 2.6  3, 2.5  2, 3.5  4
  Round like you learned in grade school (nearest representable number)…
  …except if the value is right on the borderline, in which case we round to the nearest EVEN number
  Ensures fairness on calculation, balances out inaccuracies.
    On a tie, half the time we round up; the other half time we round down.
Examples in decimal
(but applies to IEEE754 binary)
Under the hood

## Slide 6: FP Addition
More difficult than with integers
Can’t just add significands…
How do we do it?
  De-normalize to match exponents
  Add significands together
  Keep the matched exponent
  Normalize (possibly changing exponent)
Note: If signs differ, just perform a subtract instead.
Under the hood

## Slide 7: Casting floats to ints and vice versa
(int) floating_point_expression
  Coerces and converts floating point to nearest integer (C uses truncation).
  i = (int) (3.14159 * f);
(float) integer_expression
  Converts integer to nearest floating point.
  f = f + (float) i;

## Slide 8: Double Casting Doesn’t Always Work
Will not always print “true”!
Most large values of integers don’t have exact floating point representations.
  Recall: only 223 floats per exponent
What about double?
int i = …;
if (i == (int)((float) i))
{
printf("true");
}

## Slide 9: Double Casting Doesn’t Always Work
Will not always print “true”!
Most large values of integers don’t have exact floating point representations.
  Recall: only 223 floats per exponent
What about double?
int i = …;
if (i == (int)((float) i))
{
printf("true");
}
Will not always print “true”!
Small floating point numbers (<1) don’t have integer representations.
For other numbers, rounding errors…
float f = …;
if (f == (float)((int) f))
{
printf("true");
}

## Slide 10: Now you can make float jokes too…
Saturday Morning Breakfast Comics
www.smbc-comics.com/comic/2013-06-05
Side note: the robot is using IEEE 754 double-precision.
(double) 0.3:
0.29999999999999999
(double) 0.1 + (double) 0.2:
0.30000000000000004

## Slide 11: (change of gears)

## Slide 12: The RISC-V Instruction Set Architecture
Floating Point Discussion
The RISC-V Instruction Set Architecture
Elements of Architecture: Registers
Add/Sub Instructions
Immediates

## Slide 13: Great Idea #1: Abstraction (Levels of Representation/Interpretation)
lw x3, 0(x10)
lw x4, 4(x10)
sw x4, 0(x10)
sw x3, 4(x10)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., RISC-V)
Machine Language Program (RISC-V)
Compiler
Assembler
Hardware Architecture Description (e.g., block diagrams)
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
1000 1101 1110 0010 0000 0000 0000 0000
1000 1110 0001 0000 0000 0000 0000 0100
1010 1110 0001 0010 0000 0000 0000 0000
1010 1101 1110 0010 0000 0000 0000 0100
IMEM
ALU
Imm
.
Gen
+4
DMEM
Branch
Comp.
Reg
[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst
[11:7]
inst
[19:15]
inst
[24:20]
inst
[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg
[rs1]
pc
imm
[31:0]
Reg
[rs2]
wb
Anything can be represented as a number, i.e., data or instructions

## Slide 14: Assembly Language
Basic job of a CPU: execute lots of instructions.
Instructions are the primitive operations that the CPU may execute.
  Like a sentence: operations (verbs) applied to operands (objects), processed in sequence …
Different CPUs implement different sets of instructions. The set of instructions a particular CPU implements is an Instruction Set Architecture (ISA).
  Examples: ARM (cell phones), Intel x86 (i9, i7, i5, i3), IBM/Motorola PowerPC (old Macs), MIPS, RISC-V, ...

## Slide 15: Book: Programming From the Ground Up
“A new book was just released which is based on a new concept – teaching computer science through assembly language (Linux x86 assembly language, to be exact). This book teaches how the machine itself operates, rather than just the language. I've found that the key difference between mediocre and excellent programmers is whether or not they know assembly language. Those that do tend to understand computers themselves at a much deeper level. Although [almost!] unheard of today, this concept isn't really all that new -- there used to not be much choice in years past. Apple computers came with only BASIC and assembly language, and there were books available on assembly language for kids. This is why the old-timers are often viewed as 'wizards': they had to know assembly language programming.” -- slashdot.org comment, 2004-02-05

## Slide 16: Instruction Set Architectures
Early trend was to add more and more instructions to new CPUs to do elaborate operations.
  VAX architecture had an instruction to multiply polynomials!
Reduced Instruction Set Computer (RISC) philosophy:
  Cocke IBM, Patterson, Hennessy, 1980s.
  Keep the instruction set small and simple, makes it easier to build fast hardware.
  Let software do complicated operations by composing simpler ones.
  This went against the conventional wisdom of the time. (he who laughs last, laughs best)
Notes: https://en.wikipedia.org/wiki/VAX
John Cocke IBM 801 1980 - This was not well publicized as it was an internal company project.
John Hennessey Stanford MIPS 1981
David Patterson Berkeley RISC 1980

## Slide 17: Patterson and Hennessy win Turing!
https://engineering.berkeley.edu/news/2018/06/patterson-wins-turing-award/
Notes: 2017: For pioneering a systematic, quantitative approach to the design and evaluation of computer architectures with enduring impact on the microprocessor industry.
Patterson first met John Hennessy at a meeting for DARPA funded research VLSI projects in 1980 or 1981 where each was presenting their ideas. RISC-2 emerged simultaneously with Hennessy’s MIPS (Microprocessor without Interlocked Pipeline Stages) prototype at Stanford in 1983. Arguments between RISC vs. MIPS designs were soon dwarfed by their common thesis against CISC (Complex Instruction Set Computers), used by the entire industrial computer design community.
https://amturing.acm.org/award_winners/patterson_2316693.cfm
https://amturing.acm.org/award_winners/hennessy_1426931.cfm

## Slide 18: RISC-V Architecture
New open-source, license-free ISA spec
  Supported by growing shared software ecosystem
  Appropriate for all levels of computing system, from microcontrollers to supercomputers
  32-bit, 64-bit, and 128-bit variants (class/textbook uses 32-bit)
Why RISC-V instead of Intel x86-64?
  RISC-V is simple and elegant. We don’t need to get bogged down in gritty details.
  RISC-V has exponential adoption, from microcontrollers to CPUs to warehouse-scale computers.
RISC-V Green Card
IBM 360 Green Card
https://cs61c.org/  Resources

## Slide 19: RISC-V Origins
Started in Summer 2010 to support open research and teaching at UC Berkeley
  Lineage can be traced to RISC-I/II projects (1980s)
As the project matured, it migrated to RISC-V foundation (www.risc-v.org)
Many commercial and research projects based on RISC-V.
  Open-source and proprietary
  Widely used in education
Read more:
  https://riscv.org/risc-v-history/
  https://riscv.org/risc-v-genealogy/
RISC-I
RISC-II

## Slide 20: Elements of Architecture: Registers
Floating Point Discussion
The RISC-V Instruction Set Architecture
Elements of Architecture: Registers
Add/Sub Instructions
Immediates

## Slide 21: Instruction Set
Instruction set for a particular architecture (e.g. RISC-V) is represented by the assembly language.
Each line of assembly code represents one instruction for the computer.
“instruction sets”
add x1, x2, x3
operation name
registers

## Slide 22: Higher-Level Language vs. Assembly Language (1/2)
In C (and most high-level languages), variables declared first and given a type.
  int fahr, celsius; char a, b, c, d, e;
Each variable can ONLY represent a value of the type it was declared as (cannot mix/match int/char variables).
In high-level languages, variable types determine operation.
  int *p = …; p = p + 2; int x = 42; x = 3 * x;
Assembly operands are registers.
  Registers are limited number of special locations, built directly into the hardware.
  RISC-V: Operations can only be performed on register operands.
In assembly language, the registers have no type.
  Register contents are just bits.
Operation determines “type,” i.e., how register contents are treated.
  E.g., as value, memory address, etc.
C, Java
RISC-V

## Slide 23: Registers are Inside the Processor
Processor-Memory Interface
I/O-Memory Interfaces
Benefit: Since registers are directly in hardware, they’re very fast (faster than 0.25ns).
  Speed of light: 3x108m/s = 0.3m/ns = 30cm/ns = 10cm/0.3ns!!!
  0.3ns is the clock period of a 3.33GHz computer
Notes: Apple M1 Chip is 3.1 GHz max clock rate
7/10 nm transistor density

## Slide 24: Great Idea #3: Principle of Locality / Memory Hierarchy
Extremely fast
Extremely expensive Tiny capacity
Processor chip
Storage Latency Analogy

## Slide 25: 32 Registers in RISC-V
Drawback: Each ISA a predetermined number of registers.
  Why? Registers are built into hardware.
  Solution: RISC-V code must be very carefully put together to efficiently use registers.
    Nowadays: compiler maps C variables to RISC-V registers across declarations, function calls, etc.
32 registers in RISC-V.
  Why 32? Smaller is faster, but too small is bad.
  Goldilocks principle (“This porridge is too hot; This porridge is too cold; this porridge is just right”)
Each RISC-V register is 32 bits wide (in RV32 variant).
  Groups of 32 bits called a word in RV32.

## Slide 26: Register Names and Numbers
Registers are numbered from 0 to 31.
  Referred to by number x0 – x31.
x0 is special, always holds value zero.
  So only 31 registers able to hold variable values.
Each register can be referred to by number or name.
  We’ll explain names next week.
Ok, enough already…gimme my RV32!!!

## Slide 27: Add/Sub Instructions
Floating Point Discussion
The RISC-V Instruction Set Architecture
Elements of Architecture: Registers
Add/Sub Instructions
Immediates

## Slide 28: Higher-Level Language vs. Assembly Language (2/2)
Each line can contain multiple operations.
  a = b * 2 - (arr[2] + *p);
Common operations are:
  =, +, –, *, /
  Here, * includes both multiply and dereference
Each statement is an instruction.
  An instruction executes exactly one short list of simple commands.
Each line of assembly code contains at most 1 instruction.
  add x1, x2, x3
  sub x1, x1, x4
C, Java
RISC-V
The compiler translates from higher-level language down to assembly… …so RISC-V instructions are often closely related to common C/Java operations.

## Slide 29: RISC-V Arithmetic Instruction Syntax
Syntax is rigid:
  1 operator, 3 operands.
  Why? Keep hardware simple via regularity. (more in a few weeks)
opname rd, rs1, rs2
operation, by name
”destination”
operand getting result
”source1”
1st operand for operation
”source2”
2nd operand for operation

## Slide 30: RISC-V Addition and Subtraction
opname rd, rs1, rs2
operation, by name
”destination”
operand getting result
”source1”
1st operand for operation
”source2”
2nd operand for operation
Addition
Subtraction
RISC-V
C
add x1,x2,x3
a = b + c;
RISC-V
C
sub x4,x5,x6
d = e – f;
(remember!
order of operands matter in sub)

## Slide 31: RISC-V Arithmetic, Example 1
How could we translate this C statement?
a = b + c + d - e;
  Assume the above mapping for C variables ↔︎ RISC-V registers.
Solution: Break into multiple instructions!
  add x10, x1, x2 # a_temp = b + c
  add x10, x10, x3 # a_temp = a_temp + d
  sub x10, x10, x4 # a = a_temp - e
A single line of C may break up into several lines of RISC-V.
In-line comments prefixed by #, work like C99’s //.
Unlike C, no multi-line comment (/* */) support.
x10 x1 x2 x3 x4

## Slide 32: RISC-V Arithmetic, Example 2
How do we do this?
f = (g + h) - (i + j);
  Assume the above mapping for C variables ↔︎ RISC-V registers.
Solution: Use intermediate temporary registers!
  add x5, x20, x21 # a_temp = g + h
  add x6, x22, x23 # b_temp = i + j
  sub x19, x5, x6 # f = (g + h)- (i + j)
Note: A good compiler may actually do the following. Why?
f = g + h - i - j;
x19 x20 x21 x22 x23 x5 x6
Can use zero temp registers!

## Slide 33: Aside: Apollo Guidance Computer
Margaret Hamilton Director of Software Engineering Division of MIT Instrumentation Laboratory
  Built Apollo Guidance Computer Command Module (navigation, lunar landing)
    72KB of memory on board Eagle (Apollo 11, 1969)
Margaret Hamilton and Apollo code
Wikimedia Commons
https://abcnews.go.com/Technology/apollo-11s-source-code-tons-easter-eggs-including/story?id=40515222
ignition file
Presidential Medal of Freedom (2016)
Notes: https://www.smithsonianmag.com/smithsonian-institution/margaret-hamilton-led-nasa-software-team-landed-astronauts-moon-180971575/
https://www.ibiblio.org/apollo/assembly_language_manual.html
Obama is 6’2”

## Slide 34: Immediates
Floating Point Discussion
The RISC-V Instruction Set Architecture
Elements of Architecture: Registers
Add/Sub Instructions
Immediates

## Slide 35: Immediates
Immediates are numerical constants.
  They appear often in code; hence, they have separate instructions.
Add Immediate instruction:
RISC-V
C
addi x3,x4,10
f = g + 10;
Syntax similar to add instruction. But the last operand must be a number, not a register.

## Slide 36: Immediates
Immediates are numerical constants.
  They appear often in code; hence, they have separate instructions.
Add Immediate instruction:
There is no Subtract Immediate instruction in RISC-V. Why?
  While there are add and sub instructions, to subtract an immediate, just use addi:
RISC-V
C
addi x3,x4,10
f = g + 10;
Syntax similar to add instruction. But the last operand must be a number, not a register.
RISC-V
C
addi x3,x4,-10
f = g - 10;
RISC Philosophy: Reduce the possible types of operations to an absolute minimum.
If an operation can be decomposed into a simpler operation, don’t include it in the ISA.
Notes: RISC: reduced instruction set computer

## Slide 37: Register Zero
One particular immediate, the number zero (0), appears very often in code.
RISC-V hardwires the register zero (x0) to value 0:
Defined in hardware, so an instruction add x0,x3,x4 will not do anything!
RISC-V
C
add x3,x4,x0
f = g;
RISC-V
C
addi x3,x0,0xff
f = 0xff;

## Slide 38: Concept Check: True or False?
Types are associated with declaration in C (normally), but are associated with instructions (operators) in RISC-V.
Since there are only 32 registers, we can’t write RISC-V for C expressions that contain > 32 variables.
If p (stored in x9) were a pointer to an array of ints, then p++; would be addi x9 x9 1
123
FFF
FFT
FTF
FTT
TFF
TFT
TTF
TTT

## Slide 39: Concept Check: True or False?
Types are associated with declaration in C (normally), but are associated with instructions (operators) in RISC-V.
Since there are only 32 registers, we can’t write RISC-V for C expressions that contain > 32 variables.
If p (stored in x9) were a pointer to an array of ints, then p++; would be addi x9 x9 1
123
FFF
FFT
FTF
FTT
TFF
TFT
TTF
TTT
1. True, we saw that on an earlier slide.
2. False. we saw how to break up longer equations to smaller ones already.
3. False. Don’t forget that ints are (usually) 4 bytes wide, so instruction would be addi x9, x9, 4.
Notes: 1. True, we saw that on an early slide.
2. False. we saw how to break up longer equations to smaller ones already.
3. False. Don’t forget that ints are (usually) 4 bytes wide.