## Slide 1: RISC V Datapath I

## Slide 2: Building a RISC-V Processor
Building a RISC-V Processor
CPU Elements and Stages
R-Type: add datapath
R-Type: sub datapath
Datapath with immediates: addi

## Slide 3: Great Idea #1: Abstraction (Levels of Representation/Interpretation)
lw x3, 0(x10)
lw x4, 4(x10)
sw x4, 0(x10)
sw x3, 4(x10)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., RISC-V)
Machine Language Program (RISC-V)
Compiler
Assembler
Hardware Architecture Description (e.g., block diagrams)
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
1000 1101 1110 0010 0000 0000 0000 0000
1000 1110 0001 0000 0000 0000 0000 0100
1010 1110 0001 0010 0000 0000 0000 0000
1010 1101 1110 0010 0000 0000 0000 0100
IMEM
ALU
Imm
.
Gen
+4
DMEM
Branch
Comp.
Reg
[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst
[11:7]
inst
[19:15]
inst
[24:20]
inst
[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg
[rs1]
pc
imm
[31:0]
Reg
[rs2]
wb

## Slide 4: Old-school Machine Structures
CS61C
I/O system
Processor
Compiler
Operating
System
(Mac OSX)
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
Transistors
Memory
Hardware
Software
Assembler
Fabrication

## Slide 5: New-school Machine Structures
Software
Parallel Requests
Assigned to computer
  e.g., Search “Cats”
Parallel Threads
Assigned to core e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions All gates work in parallel at same time
Smart Phone
Warehouse Scale Computer
Hardware
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Exec. Unit(s)
Functional
Block(s)
A0+B0
A1+B1
Logic Gates
Harness Parallelism &
Achieve High Performance

## Slide 6: How do we build a Single-Core Processor?
Processor (CPU): the active part of the computer that does all the work (data manipulation and decision-making).
  Datapath (“the brawn”): portion of the processor that contains hardware necessary to perform operations required by the processor.
  Control (“the brain”): portion of the processor (also in hardware) that tells the datapath what needs to be done.
Notes: Apple M1 Chip is 3.1 GHz max clock rate
7/10 nm transistor density
FOR NEXT TIME: switch control and datapath descriptions to match visual layout

## Slide 7: Goal: Design HW to Execute All RV32I Instructions
Open Reference Card |  |  |  |  | 
Base Integer Instructions: RV32I |  |  |  |  | 
Category Name | Fmt | RV32I Base | Category Name | Fmt | RV32I Base
Shifts Shift Left Logical | R | SLL rd,rs1,rs2 | Loads Load Byte | I | LB rd,rs1,imm
Shift Left Log. Imm. | I | SLLI rd,rs1,shamt | Load Halfword | I | LH rd,rs1,imm
Shift Right Logical | R | SRL rd,rs1,rs2 | Load Byte Unsigned | I | LBU rd,rs1,imm
Shift Right Log. Imm. | I | SRLI rd,rs1,shamt | Load Half Unsigned | I | LHU rd,rs1,imm
Shift Right Arithmetic | R | SRA rd,rs1,rs2 | Load Word | I | LW rd,rs1,imm
Shift Right Arith. Imm. | I | SRAI rd,rs1,shamt | Stores Store Byte | S | SB rs1,rs2,imm
Arithmetic ADD | R | ADD rd,rs1,rs2 | Store Halfword | S | SH rs1,rs2,imm
ADD Immediate | I | ADDI rd,rs1,imm | Store Word | S | SW rs1,rs2,imm
SUBtract | R | SUB rd,rs1,rs2 | Branches Branch = | B | BEQ rs1,rs2,imm
Load Upper Imm | U | LUI rd,imm | Branch ≠ | B | BNE rs1,rs2,imm
Add Upper Imm to PC | U | AUIPC rd,imm | Branch < | B | BLT rs1,rs2,imm
Logical XOR | R | XOR rd,rs1,rs2 | Branch ≥ | B | BGE rs1,rs2,imm
XOR Immediate | I | XORI rd,rs1,imm | Branch < Unsigned | B | BLTU rs1,rs2,imm
OR | R | OR rd,rs1,rs2 | Branch ≥ Unsigned | B | BGEU rs1,rs2,imm
OR Immediate | I | ORI rd,rs1,imm | Jump & Link J&L | J | JAL rd,imm
AND | R | AND rd,rs1,rs2 | Jump & Link Register | I | JALR rd,rs1,imm
AND Immediate | I | ANDI rd,rs1,imm |  |  | 
Compare Set < | R | SLT rd,rs1,rs2 | Synch Synch thread | I | FENCE
Set < Immediate | I | SLTI rd,rs1,imm |  |  | 
Set < Unsigned | R | SLTU rd,rs1,rs2 | Environment CALL | I | ECALL
Set < Imm Unsigned | I | SLTIU rd,rs1,imm | BREAK | I | EBREAK
Not in this class
HiFive Unmatched (RISC-V Linux)
https://www.sifive.com/boards/hifive-unmatched

## Slide 8: CPU Elements and Stages
Building a RISC-V Processor
CPU Elements and Stages
R-Type: add datapath
R-Type: sub datapath
Datapath with immediates: addi

## Slide 9: Combinational Logic Blocks
Today, we will think of all combinational logic subcircuits as block diagrams:
1-bit-wide 2-to-1MUX
1
0
N
N
a
b
N
c
s
32-bit-wide 2-to-1 MUX
Review
Simple ALU (add,sub,and,or)
ALU (ALUOp selects from multiple operations)
N-Bit Adder
A
ALU
B
AluOp
Result
A
Add
B
32
32
32
CarryIn
A
B
CarryOut
S
32-Bit Adder

## Slide 10: One-Instruction-Per-Cycle RISC V Machine
The CPU is composed of two types of subcircuits: combinational logic blocks and state elements.
On every tick of the clock, the computer executes one instruction:
  Current outputs of the state elements drive the inputs to combinational logic…
  …whose outputs settle at the inputs to the state elements before the next rising clock edge.
At the rising clock edge:
  All the state elements are updated with the combinational logic outputs…
  and execution moves to the next clock cycle.
Combinational logic
PC
IMEM
Reg[ ]
DMEM
clk

## Slide 11: State Elements Required by RV32I ISA
Memory MEM
IMEM
DMEM
During CPU execution, each RV32I instruction reads and/or updates these state elements.
PC
Program Counter
Register File Reg
Reg[ ]

## Slide 12: State Elements (1/3): Program Counter
Register File Reg
Memory MEM
PC
IMEM
DMEM
Reg[ ]
Program Counter
clk
Data In
Write Enable
N
N
Data Out
A register in Logisim
The Program Counter is a 32-bit Register.
  Input:
    N-bit data input bus
    Write Enable “Control” bit (1: asserted/high, 0: deasserted/0)
  Output:
    N-bit data output bus
  Behavior:
    If Write Enable is 1 on rising clock edge, set Data Out=Data In.
    At all other times, Data Out will not change; it will output its current value.

## Slide 13: State Elements (2/3): Register File
Register File (RegFile) has 32 registers.
  Input:
    One 32-bit input data bus, dataW.
    Three 5-bit select busses, rs1, rs2, and rsW.
    RegWEn control bit.
  Output:
    Two 32-bit output data busses, data1 and data2.
Register File Reg
Memory MEM
PC
IMEM
DMEM
Reg[ ]
Program Counter
dataW
rsW
rs1 data1
rs2
data2
Reg[]
clk
32
32
5
5
5
32
  Registers are accessed via their 5-bit register numbers:
    R[rs1]: rs1 selects register to put on data1 bus out.
    R[rs2]: rs2 selects register to put on data2 bus out.
    R[rd]: rsW selects register to be written via dataW when RegWEn=1.
  Clock behavior: Write operation occurs on rising clock edge.
    Clock input only a factor on write!
    All read operations behave like a combinational block:
        If rs1, rs2 valid, then data1, data2 valid after access time.
RegWEn
RegFile behaves like a combinational block for read operations!

## Slide 14: State Elements (3/3): Memory
  Memory words are accessed as follows:
    Read: Address addr selects word to put on dataR bus.
    Write: Set MemRW=1. Address addr selects word to be written with dataW bus.
  Like RegFile, clock input is only a factor on write.
    If MemRW=1, write occurs on rising clock edge.
    If MemRW=0 and addr valid, then dataR valid after access time.
Memory is “magic.” For this class:
  32-bit byte-addressed memory space; and
  Memory access with 32-bit words.
Register File Reg
Memory MEM
PC
IMEM
DMEM
Reg[ ]
Program Counter
If MemRW=0, MEM behaves like a combinational block.
dataR
addr
MEM
dataW
clk
MemRW
32
32
32
Notes: Note: What happens with sb? (answer: only the lowest byte in the register is taken, and only that byte in memory changes). Similar for sh.

## Slide 15: “Two” Memories: IMEM, DMEM
Register File Reg
Memory MEM
PC
IMEM
DMEM
Reg[ ]
Program Counter
dataR
addr
MEM
dataW
clk
addr
inst
IMEM
MemRW
32
32
32
dataR
addr
DMEM
dataW
clk
MemRW
32
32
32
32
32
  Current abstraction: Memory holds both instructions and data in one contiguous 32-bit memory space.
  In our processor, we’ll use two “separate” memories:
    IMEM: A read-only memory for fetching instructions.
    DMEM: A memory for loading (read) and storing (write) data words.
    Under the hood, these are placeholders for caches. (more later)
  Because IMEM is read-only, it always behaves like a combinational block:
    If addr valid, then instr valid after access time.

## Slide 16: Design the Datapath in Phases
Task: “Execute an instruction.”
  All necessary operations, starting with fetching the instruction.
Problem: A single “monolithic” block would be bulky and inefficient.
Solution: Break up the process into stages, then connect the stages to create the whole datapath.
  Smaller stages are easier to design!
  Modularity: Easy to optimize one stage without touching the others.
Combinational logic
PC
IMEM
Reg[ ]
DMEM
clk
(hard to implement this block diagram as-is)

## Slide 17: 5 Basic Stages (Phases) of Instruction Execution
We will implement a single-cycle processor:
  All stages of one RV32I instruction execute within the same clock cycle.
PC
Reg[ ]
DMEM
ALU
IMEM
1. Instruction Fetch (IF)
  2. Instruction Decode (ID)
    + Read Registers
  3. Execute (EX)
  Arithmetic Logic Unit (ALU)
  4. Memory Access (MEM)
  5. Write back to Register (WB)
clk

## Slide 18: Not All Instructions Need All 5 Stages!
PC
Reg[ ]
DMEM
ALU
IMEM
1. Instruction Fetch (IF)
  2. Instruction Decode (ID)
    + Read Registers
  3. Execute (EX)
  Arithmetic Logic Unit (ALU)
  4. Memory Access (MEM)
  5. Write back to Register (WB)
Control Logic
The control logic selects “needed” datapath lines based on the instruction.
  MUX selector, ALU op selector, write enable, etc.

## Slide 19: R-Type: add Datapath
Building a RISC-V Processor
CPU Elements and Stages
R-Type: add datapath
R-Type: sub datapath
Datapath with immediates: addi

## Slide 20: Implementing the add Instruction
Suppose we had a single instruction in our RISC-V ISA: add.
The add instruction makes two changes to processor state:
  RegFile Reg[rd] = Reg[rs1] + Reg[rs2]
  PC PC = PC + 4
Example add-only program | Assembly instructions
0x100 | add x18,x18,x10
0x108 | add x18,x18,x18
… | add …
add rd, rs1, rs2
31 |  |  |  | 25 | 24 |  | 20 | 19 |  | 15 | 14 | 12 | 11 |  | 7 | 6 |  |  |  | 0
funct7 |  |  |  |  |  |  |  |  |  |  | funct3 |  |  |  |  | opcode |  |  |  | 
0000000 |  |  |  |  | rs2 |  |  | rs1 |  |  | 000 |  | rd |  |  | 0110011 |  |  |  | 
7 |  |  |  |  | 5 |  |  | 5 |  |  | 3 |  | 5 |  |  | 7 |  |  |  | 
“add”
Reg-Reg opcode
“add”

## Slide 21: Datapath for add
R[rs1]
R[rs2]
add
inst[11:7]
inst[19:15]
inst[24:20]
addr
inst
IMEM
PC
clk
add
pc
+4
pc+4
clk
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
31 |  |  |  | 25 | 24 |  | 20 | 19 |  | 15 | 14 | 12 | 11 |  | 7 | 6 |  |  |  | 0
funct7 |  |  |  |  | rs2 |  |  | rs1 |  |  | funct3 |  | rd |  |  | 0110011 |  |  |  | 
PC = PC + 4
R[rd] = R[rs1] + R[rs2]
Increment PC to next instruction.
Write Add output to destination register.
Feed read register values into Add.
Split instruction to index into RegFile.
RegWEn
1
Control Logic
A
Add
B
Notes: For next time: emphasize when write happens
From textbook, Figure 4.7: Remember that writes are edge-triggered, so that all the write inputs (i.e, the value to be written, the register number, and the write control signal) must be valid at the clock edge. Since writrs to the register file are edge-triggered, our design can legally writ and read the same register within a clock cycle: the read will get the value written in an earlier clock cycle, while the value written will be available to read in a subsequent clock cycle.

## Slide 22: Plan: Iteratively Build Full Datapath
dataR
addr
DMEM
dataW
clk
addr
inst
IMEM
add
PC
R[rs1]
clk
clk
R[rs2]
pc
+4
add
RegWEn
1
Control Logic
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
pc+4
A
Add
B
inst[11:7]
inst[19:15]
inst[24:20]
For now, we will disconnect memory. By the end of next lecture, we’ll build the datapath that supports the full RV32I ISA.
Notes: For next time: switch with previous slide, remove wires

## Slide 23: R-Type: sub Datapath
Building a RISC-V Processor
CPU Elements and Stages
R-Type: add datapath
R-Type: sub datapath
Datapath with immediates: addi

## Slide 24: Implementing the sub Instruction
What if our ISA now had two instructions: add/sub?
sub rd, rs1, rs2
funct7 |  |  | funct3 |  | opcode | 
0000000 | rs2 | rs1 | 000 | rd | 0110011 | add
0100000 | rs2 | rs1 | 000 | rd | 0110011 | sub
sub is almost the same as add, except now the ALU subtracts operands instead of adding them:
  RegFile Reg[rd] = Reg[rs1] - Reg[rs2]
  PC PC = PC + 4
Instruction bit inst[30] selects between add/sub.
  Details left to control logic.

## Slide 25: Datapath for sub
addr
inst
IMEM
add
PC
R[rs1]
clk
clk
R[rs2]
pc
+4
alu
RegWEn
1
Control Logic
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
pc+4
A
ALU
B
inst[11:7]
inst[19:15]
inst[24:20]
31 |  |  |  | 25 | 24 |  | 20 | 19 |  | 15 | 14 | 12 | 11 |  | 7 | 6 |  |  |  | 0
0100000 |  |  |  |  | rs2 |  |  | rs1 |  |  | funct3 |  | rd |  |  | 0110011 |  |  |  | 
Increment PC to next instruction.
Write ALU output to destination register.
Feed read register values into ALU.
Split instruction to index into RegFile.
ALUSel
Sub
The control line ALUSel selects which ALU operation to output.
Convention: Add(0), Sub(1).
inst[31:0]
Pass instr to Control for instruction decoding (for now, all 32 bits).
PC = PC + 4
R[rd] = R[rs1] - R[rs2]

## Slide 26: Control vs. Datapath Analogy: Space Mission
inst[31:0]
RegWEn
1
ALUSel
Sub
Control Logic
Space Station
“Control, what should I do? Here’s the instruction.”
addr
inst
IMEM
add
PC
R[rs1]
clk
clk
R[rs2]
pc
+4
alu
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
pc+4
A
ALU
B
inst[11:7]
inst[19:15]
inst[24:20]
“RegFile, enable register write.”
“ALU, perform Sub op.”
Mission Control
Control and Datapath are two abstractions that together comprise the CPU. Under the hood, both are designed with combinational logic and/or state elements.

## Slide 27: Supporting all R-Type Instructions
funct7 |  |  | funct3 |  | opcode | 
0000000 | rs2 | rs1 | 000 | rd | 0110011 | add
0100000 | rs2 | rs1 | 000 | rd | 0110011 | sub
0000000 | rs2 | rs1 | 001 | rd | 0110011 | sll
0000000 | rs2 | rs1 | 010 | rd | 0110011 | slt
0000000 | rs2 | rs1 | 011 | rd | 0110011 | sltu
0000000 | rs2 | rs1 | 100 | rd | 0110011 | xor
0000000 | rs2 | rs1 | 101 | rd | 0110011 | srl
0100000 | rs2 | rs1 | 101 | rd | 0110011 | sra
0000000 | rs2 | rs1 | 110 | rd | 0110011 | or
0000000 | rs2 | rs1 | 111 | rd | 0110011 | and
A
ALU
B
The Control Logic decodes funct3, funct7 instruction fields and selects appropriate ALU function by setting the control line ALUSel.
ALUSel
add,sub,xor,and,or,slt,sltu,sll,sra,srl
Check out Project 3 for the full ALU!
Notes: rd = (rs1 < rs2) ? 1 : 0

## Slide 28: Datapath with Immediates: addi
Building a RISC-V Processor
CPU Elements and Stages
R-Type: add datapath
R-Type: sub datapath
Datapath with immediates: addi

## Slide 29: Implementing the addi Instruction
Suppose we add a new instruction: addi, RV32I I-Format:
The addi instruction updates the same two states as before. But we now need to build an immediate imm!
  RegFile Reg[rd] = Reg[rs1] + imm
  PC PC = PC + 4
addi rd, rs1, imm
31 |  |  |  | 25 | 24 |  | 20 | 19 |  | 15 | 14 | 12 | 11 |  | 7 | 6 |  |  |  | 0
 |  |  |  |  |  |  |  |  |  |  | funct3 |  |  |  |  | opcode |  |  |  | 
imm[11:0] |  |  |  |  |  |  |  | rs1 |  |  | 000 |  | rd |  |  | 0010011 |  |  |  | 
12 |  |  |  |  |  |  |  | 5 |  |  | 3 |  | 5 |  |  | 7 |  |  |  | 
OP-IMM
“add”

## Slide 30: What Does the Datapath Need for addi?
addr
inst
IMEM
add
PC
R[rs1]
clk
clk
R[rs2]
pc
+4
alu
inst[31:0]
RegWEn
1
ALUSel
Add
Control Logic
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
pc+4
To compute alu = R[rs1] + imm…
…we should feed in an immediate to ALU input B (instead of R[rs2]).
A
ALU
B
inst[11:7]
inst[19:15]
inst[24:20]
✅
PC = PC + 4
R[rd] = R[rs1] + imm

## Slide 31: 1. New MUX to Select Immediate for ALU
addr
inst
IMEM
add
PC
R[rs1]
clk
clk
R[rs2]
pc
+4
alu
inst[31:0]
RegWEn
1
Control Logic
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
pc+4
A
ALU
B
inst[11:7]
inst[19:15]
inst[24:20]
0
1
imm
Bsel
1
ALUSel
Add
1. Control line Bsel=1 selects the generated immediate imm for ALU input B.

## Slide 32: 2. New Block to Generate 32-bit Immediate
addr
inst
IMEM
add
PC
R[rs1]
clk
clk
R[rs2]
pc
+4
alu
inst[31:0]
RegWEn
1
Control Logic
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
pc+4
A
ALU
B
inst[11:7]
inst[19:15]
inst[24:20]
0
1
Bsel
1
Split and get the upper 12 bits of instr.
inst[31:20]
imm[31:0]
ImmSel
I
Imm. Gen
ALUSel
Add
1. Control line Bsel=1 selects the generated immediate imm for ALU input B.
2. Immediate Generation Block builds a 32-bit immediate imm from instruction bits.

## Slide 33: Tracing/Lighting the addi Datapath
Imm. Gen
inst[31:20]
addr
inst
IMEM
add
PC
inst[11:7]
inst[19:15]
inst[24:20]
R[rs1]
clk
clk
R[rs2]
imm[31:0]
pc
+4
inst[31:0]
ImmSel
RegWEn
Bsel
ALUSel
Control Logic
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
pc+4
0
1
Imm. Gen
A
ALU
B
alu
R[rs2]
pc
Data inst[24:20] still feeds into Reg[], which still outputs R[rs2].
However, control Bsel=1 means R[rs2] data line is ignored.
Increment PC to next instruction.
Write ALU output to destination register.
Control line Bsel=1 selects the generated immediate imm for ALU input B.
Immediate Generation Block builds a 32-bit immediate imm from instruction bits.
ImmSel
I
RegWEn
1
Bsel
1
ALUSel
Add

## Slide 34: Immediate Generation Block Design
(more next time)
inst[31:20]
imm[31:0]
Imm. Gen
Instruction inst[31:0]
31 | 30 |  |  |  |  |  | 20 | 19 |  | 15 | 14 | 12 | 11 |  | 7 | 6 |  |  |  | 0
imm[11:0] | imm[10:0] |  |  |  |  |  |  | rs1 |  |  | funct3 |  | rd |  |  | opcode |  |  |  | 
s | ... .... .... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  |  |  |  | 12 | 11 |  |  |  |  |  |  | 0
imm[31:12] |  |  |  |  |  |  |  |  |  |  |  |  | imm[11:0] |  |  |  |  |  |  | 
ssss ssss ssss ssss ssss |  |  |  |  |  |  |  |  |  |  |  |  | s... .... .... |  |  |  |  |  |  | 
Copy upper 12 bits of instruction, inst[31:20], to lower 12 bits of immediate, imm[11:0].
Immediate imm[31:0]
Sign-extend: Copy inst[31] to upper 20 bits of immediate, imm[31:12].

## Slide 35
Notes: Do not modify the notes in this section to avoid tampering with the Poll Everywhere activity. More info at polleverywhere.com/support Datapath Design I
https://www.polleverywhere.com/multiple_choice_polls/iSgOoVAN9UVbGcYUiWrbY?state=opened&flow=Default&onscreen=persist

## Slide 36: Your Own Design
We should use the main ALU to compute PC=PC+4 in order to save some gates.
The ALU is a synchronous state element.
The program counter (PC) is a register.
  123
  FFF
  FFT
  FTF
  FTT
  TFF
  TFT
  TTF
  TTT

## Slide 37: Summary: Arithmetic/Logical Datapath
Imm. Gen
inst[31:20]
All data lines carry information.
Control logic determines what is “useful/needed” vs. what is “ignored.”
  e.g., ALUSel: chooses ALU operation; Bsel: chooses register/immediate for ALU input B.
addr
inst
IMEM
add
PC
inst[11:7]
inst[19:15]
inst[24:20]
R[rs1]
clk
clk
R[rs2]
imm[31:0]
pc
+4
inst[31:0]
ImmSel
I: I-Type
(more next time)
RegWEn
1
Control Logic
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
pc+4
0
1
Imm. Gen
A
ALU
B
alu
R[rs2]
pc
Bsel
0: R[rs1]
1: imm
ALUSel
add,sub,xor,and,or,
slt,sltu,sll,sra,srl

## Slide 38: Our Single-Core Processor So Far…
C
on
t
r
ol
D
a
t
ap
at
h
P
r
o
g
r
am
C
oun
t
er (PC)
R
egi
s
t
e
r
s
A
r
i
t
hm
e
t
i
c
-Logic
U
nit
(
A
L
U)
P
r
o
c
e
s
sor
Memo
r
y
Enabl
e
?
R
ead
/
W
r
i
t
e
A
dd
r
e
s
s
W
r
i
t
e
D
a
t
a
R
ead
D
a
t
a
I
n
put
Ou
t
put
B
y
t
e
s
P
r
o
g
r
am
D
a
t
a