## Slide 1: Pipeline III: More Hazards, Superscalar Processors
Post-Miderm Ed Post:
Do not talk about the exam
Reach out to cs61c@berkeley.edu with any exam-related concerns
Student Support appointment meetings (non-exam related) are open

## Slide 2: Talk announcement! Prof. Jae W. Lee
SLICE Lab Meeting, Wednesday 10/19/22, 1:05 PM on Zoom
Specialized Architectures for Machine Learning and Data Analytics
  Abstract: In this talk I will introduce some of my recent work on domain-specific hardware accelerators and systems, especially in the domains of machine learning and data analytics. With the end of Moore's Law and Dennard Scaling, specialization of hardware, algorithm and software stack has become the primary source of additional performance, and we start seeing an explosion of novel computer architectures. With this trend my research group has recently proposed various hardware accelerators and/or specialized software stacks in these domains. At the beginning of the talk, I will identify some of the challenges in designing scalable ML/data analytics computing platforms and briefly overview our work addressing these challenges. And then, I will present in greater depth a couple of case studies of hardware/software co-design---one from ML and the other from data analytics.
  Bio: I am a Professor of CSE at Seoul National University (SNU), South Korea, and a Visiting Faculty Researcher at Google Brain, Mountain View, USA. I have received my Ph.D. degree in CS from MIT under supervision of Krste Asanovic, M.S. degree in EE from Stanford, and B.S. degree in EE from SNU. I am a computer architect by training and working at the intersection of hardware, system software and algorithms to make computers faster and more cost/energy-efficient, with emphasis on ML and data analytics applications. I worked on various projects in the past, including MIT Raw microprocessor, first silicon PUF (Physically Unclonable Function), architecture support for dynamic information flow tracking (DIFT), QoS-capable uncore design, tagless DRAM cache architectures, self-attention/garbage collection/(de)serialization/search/ genomics/page-fault handling/... /hardware accelerators, to name a few. (Sorry - they were not "a few".)

## Slide 3: Data Hazards II: Forwarding
Data Hazards II: Forwarding
Data Hazards III: Load
Control Hazards
Superscalar Processors and Measuring CPI

## Slide 4: MEM/WB Pipeline Registers
addr
inst
IMEM
A
ALU
B
Branch Comp.
add
Imm. Gen
PC
dataR
addr
DMEM
dataW
clk
clk
aluMEM
rs2EX
immEX
+4
1
0
0
1
0
1
clk
+4
2
1
0
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
rs1EX
PCEX
PCMEM
rs2MEM
instEX
instID
PCID
add
PC+4WB
aluWB
instMEM
instWB
IF
  ID
  EX
  MEM
  WB
memWB
Review
Pipeline registers allow multiple instructions to execute in separate stages.
IF/ID
ID/EX
EX/MEM
MEM/WB
sub t2,s0,t0
add s0,t0,t1
Notes: IF/ID: 32-b PC address, 32-b instruction
ID/EX: immediate, R[rs1], R[rs2], PC address, 32-b instruction
EX/MEM: R[rs2], PC, ALU, instruction
MEM/WB: ALU, mem, PC+4, instruction

## Slide 5: Data Hazards, Solution 1: Stalling
add s0,t0,t1
sub t2,s0,t0
or t6,s0,t3
5
5
5
5
5/9
9
s0 value
✅
9
9
9
Solution 1: Stall pipeline:
  Requires extra pipeline state to prevent register writes on stalled stages.
  The correct instruction is stalled for two clock cycles.
time
Problem: Instruction depends on WB’s RegFile write from previous instruction.
  Executing sub immediately after and reads old value of s0.
add s0,t0,t1
sub  nop
sub  nop
sub t2,s0,t0
or t6,s0,t3
⚠️
⚠️
Review
✅
Notes: Note: stalls are like explicit nops (addi x0,x0,0), except the latter requires more code space.
A hazard is a situation in which a planned instruction cannot execute in the “proper” clock cycle.

## Slide 6: Solution 2: Forwarding
add s0,t0,t1
sub t2,s0,t0
or t6,s0,t3
5
5
5
5
5/9
9
s0 value
9
9
9
9
Forwarding, aka bypassing, uses the result when it is computed.
  Don’t wait for value to be stored into RegFile.
  Instead, grab operand from the pipeline stage.
time
Implementation:
  Make extra connections in the datapath.
  Also add forwarding control logic.
9

## Slide 7: Forwarding EX Results
(MEM Forwarding is similar but omitted for simplicity.)
IF/ID
ID/EX
EX/MEM
MEM/WB
addr
inst
IMEM
A
ALU
B
Branch Comp.
add
Imm. Gen
PC
dataR
addr
DMEM
dataW
clk
clk
aluMEM
rs2EX
immEX
+4
0
1
clk
+4
2
1
0
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
rs1EX
PCEX
PCMEM
rs2MEM
instEX
instID
PCID
add
PC+4WB
aluWB
instMEM
instWB
memWB
Forwarding Control Logic
Bsel
Asel
If instMEM’s dest. is one of instEX source operands, forward it.

## Slide 8: Data Hazards III: Load
Data Hazards II: Forwarding
Data Hazards III: Load
Control Hazards
Superscalar Processors and Measuring CPI

## Slide 9: Forwarding Cannot Fix All Data Hazards (1/2)
add s0,t1,t2
lw s1,8(s0)
or t3,s1,t1
and t4,s1,t2
sll t0,t1,t2
✅ 1. Forward EX stage output to input of EX stage on next clock cycle.
time
✅ 2. Forward MEM stage output to input of EX stage on next clock cycle.

## Slide 10: Forwarding Cannot Fix All Data Hazards (2/2)
add s0,t1,t2
lw s1,8(s0)
or t3,s1,t1
and t4,s1,t2
sll t0,t1,t2
1. Forward EX stage output to input of EX stage on next clock cycle.
time
2. Forward MEM stage output to input of EX stage on next clock cycle.
⚠️ 3. MEM stage (lw)’s output needed as EX stage (or)’s input in the same clock cycle.
Loads can result in an unavoidable pipeline stall.
❌

## Slide 11: Data Hazard 3: Loads
time
lw s1,8(s0)
or t3,s1,t1
and t4,s1,t2
lw s1,8(s0)
or  nop
or t3,s1,t1
⚠️ MEM stage (lw)’s output needed as EX stage (or)’s input in the same clock cycle.
Forwarding sends data to the next clock cycle. Cannot go backwards in time!
The instruction slot after a load is called the load delay slot.
If this instruction uses the result of load:
  The hardware must stall for one cycle (plus forwarding).
  This results in performance loss!
❌
Load delay slot:

## Slide 12: Solution: Code Scheduling
Idea: Fix this hazard at the code compilation stage.
  In the delay slot, put an instruction unrelated to the load result.
   No performance loss!
Code scheduling: With knowledge of the underlying CPU pipeline, the compiler reorders code to improve performance.
A[3] = A[0] + A[1];
A[4] = A[0] + A[2];
C Code
✅ Alternative (7 cycles):
lw t1, 0(t0)
lw t2, 4(t0)
lw t4, 8(t0)
add t3, t1, t2
sw t3, 12(t0)
add t5, t1, t4
sw t5, 16(t0)
Forward! (+0 cycle)
⚠️ Simple compilation (9 cycles for 7 instructions)
lw t1, 0(t0)
lw t2, 4(t0)
add t3, t1, t2
sw t3, 12(t0)
lw t4, 8(t0)
add t5, t1, t4
sw t5, 16(t0)
Stall & forward! (+1 cycle)
(+1 cycle)

## Slide 13: Control Hazards
Data Hazards II: Forwarding
Data Hazards III: Load
Control Hazards
Superscalar Processors and Measuring CPI

## Slide 14: Three Types of Pipeline Hazards
A hazard is a situation in which a planned instruction cannot execute in the “proper” clock cycle.
Structural hazard:
  Hardware does not support access across multiple instructions in the same cycle.
Data hazard:
  Instructions have data dependency.
  Need to wait for previous instruction to complete its data read/write.
Control hazard:
  Flow of execution depends on previous instruction.
✅
✅

## Slide 15: Branch Results Computed During MEM
addr
inst
IMEM
A
ALU
B
Branch Comp.
add
Imm. Gen
PC
dataR
addr
DMEM
dataW
clk
clk
aluMEM
rs2EX
immEX
+4
1
0
0
1
0
1
clk
+4
2
1
0
dataW
rsW
rsR1 dataR1
rsR2
dataR2
Reg[]
rs1EX
PCEX
PCMEM
rs2MEM
instEX
instID
PCID
add
PC+4WB
aluWB
instMEM
instWB
IF
  ID
  EX
  MEM
memWB
Review
EX/MEM
PCSel
taken/not taken
  WB
  In MEM stage: EX/MEM pipeline reg. feeds IF stage MUX. PCSel control is set.
  On the next clock cycle in the IF stage, PC updates, and the correct instruction is fetched.; fetches the correct instruction.
Notes: IF/ID: 32-b PC address, 32-b instruction
ID/EX: immediate, R[rs1], R[rs2], PC address, 32-b instruction
EX/MEM: R[rs2], PC, ALU, instruction
MEM/WB: ALU, mem, PC+4, instruction

## Slide 16: Control Hazard: Conditional Branches
0x40 beq t0,t1,Label
0x44 sub t2,s0,t0
0x48 or t6,s0,t3
0x4c xor t5,t1,s0
0x70 sw s0,8(t3) # Label
Control hazards occur when the instruction fetched may not be the one needed. For example, if the beq branch is taken:
Instruction execution starts before branch outcome is known!
Correct instruction starts executing
PC updated

## Slide 17: Kill Instructions after Branch (If Taken)
0x40 beq t0,t1,Label
0x44 sub t2,s0,t0
0x48 or t6,s0,t3
0x4c xor t5,t1,s0
0x70 sw s0,8(t3) # Label
Flush pipeline by converting incorrect instructions to nops.
PC updated, correct instruction loaded

## Slide 18: Branch Prediction to Reduce Penalties
Every taken branch in the simple RV32I pipeline costs 3 clock cycles.
  Note if branch is not taken, then pipeline is not stalled; the correct instructions are correctly fetched sequentially after the branch instruction.
  (See textbook for an out of scope hardware cost improvement.)
We can improve the CPU performance on average through branch prediction.
  Early in the pipeline, guess which way branches will go.
  Flush pipeline if branch prediction was incorrect.
Notes: Side note, out of scope: Branch calculation can be moved into earlier stages to reduce ”taken branch” cost to 1 cycle. See textbook.

## Slide 19: Naïve Predictor: Don’t Take Branch
0x40 beq t0,t1,Label
0x44 sub t2,s0,t0
0x48 or t6,s0,t3
0x4c xor t5,t1,s0
0x50 add t2,s0,s0
The simple RV32I pipeline effectively always “predicts” that branches are not taken.
If branch not taken, correct instructions are already executed.
“Guess” next PC to be PC + 4
“Evaluate” guess
time
Penalty for incorrect prediction is still 3 clock cycles! Branch prediction tries to improve average performance.

## Slide 20: Superscalar Processors and Calculating CPI
Data Hazards II: Forwarding
Data Hazards III: Load
Control Hazards
Superscalar Processors and Measuring CPI

## Slide 21: Pipelining and ISA Design
The RISC-V ISA is designed for pipelining:
  All instructions are 32 bits wide.
    Easy to fetch and decode, each in one clock cycle.
    Contrast with CISC (Complex) x86: 1- to 15-byte-wide instructions!
  A small set of standard instruction formats
    Can decode/read registers in one stage.
  Load/store addressing conceptually:
    Calculate address in 3rd stage (with ALU); and
    Access memory in 4th stage.
  Memory operands are all aligned
    Memory access takes only one cycle.
The 5-stage pipeline we have studied is commonplace in many devices: cars, appliances, etc.

## Slide 22: Further Increasing Processor Performance?
Increase clock rate.
  Limited by technology and power dissipation
Increase pipeline depth.
  “Overlap” instruction execution through deeper pipeline, e.g., 10 or 15 stages.
    Less work per stage  shorter clock cycle/lower power
    But more potential for all three types of hazards! (more stalling  CPI > 1)
Design a “superscalar” processor.
  Desktops, laptops, cell phones, etc. often have a few of these, combined with simpler 5-stage pipeline processors.
Notes: Technology: How fast transistors will switch
Clock rate increase common through early 2000s, but then we hit this power ceiling, because of lack of cooling

## Slide 23: Superscalar Processors
Multiple-issue: Start multiple instructions per clock cycle.
  Multiple execution units execute instructions in parallel.
    Each execution unit has its own pipeline.
    CPI < 1: multiple instructions completed per clock cycle.
Dynamic “out-of-order” execution:
  Reorder instructions dynamically in HW to reduce impact of hazards.
Instruction fetch and decode unit
Reservation station
Reservation station
Reservation station
Reservation station
Integer
Integer
Floating Point
Load/ store
Commit unit
…
…
Take CS152 for more!
Notes: Fig 4.73, p.348: “The final step of updating the state is also called retirement or graduation.”

## Slide 24: Computing Cycles Per Instruction (CPI)
ARM Cortex-A53 Core: 2 GHz, dual-issue processor:
  4 BIPS (billion instructions per second), Peak CPI = 0.5.
  However, instruction/pipeline dependencies reduce performance.
In practice, measure CPI on various benchmarks:
  Known benchmark programs from a variety of application domains:
    Data compression, code compilation, video decoding, network simulation, etc.
From the “Iron Law” of Processor Performance:
(can count)
(can measure)
1/clock rate
CPI
We compute CPI on different benchmarks:

## Slide 25: ARM A53 Benchmark
ARM Cortex-A53 Core: 2 GHz, dual-issue processor:
  4 BIPS (billion instructions per second), Peak CPI = 0.5.
  However, instruction/pipeline dependencies reduce performance.
P&H 2nd edition, Section 4.12 (Fig 4.76, p.357)
If CPI < 1, can also measure in IPC (Instructions Per Cycle).
CPI = 1
(more next time)
Notes: Omnetpp: event simulation of a large ethernet network
mcf: min cost flow problem

## Slide 26
IMEM
Reg
Reg
ALU
IF
ID
EX
MEM
WB
DMEM
IMEM
Reg
Reg
ALU
IF
ID
EX
MEM
WB
DMEM
Single-Cycle Datapath
Pipelined Datapath
IMEM
Reg
Reg
ALU
IF
ID
EX
MEM
WB
DMEM
IMEM
Reg
Reg
ALU
IF
ID
EX
MEM
WB
DMEM
IMEM
Reg
Reg
ALU
IF
ID
EX
MEM
WB
DMEM
sw
lw
IMEM
Reg
Reg
ALU
IF
ID
EX
MEM
WB
DMEM
beq